## Slide 1: Connecting Devices

## Slide 2: The story so far
Shown why
Shown the building blocks used to build technology
Next
  Show how those building blocks enable an iPhone quality user experience
Topics
  Connecting a device to a profile
  Exchange of credentials
  Confirmation protocol (2nd factor)

## Slide 3: Basic device connection
User creates personal Mesh and account
Binds account to service ‘alice@example.com’
To connect a laptop
  On laptop: Request connection to alice@example.com
    Device shows a connection validation digest
  On admin machine
    Fetch pending messages
    Check connection validation digest matches
    Accept (or reject) the connection request
  On laptop: Complete connection.
    Device now synchronizes

## Slide 4: PIN Code authentication
Avoids then need to check validation UDFs match
On admin machine
  Request PIN code generation
On laptop
  Request connection to alice@example.com with PIN
On admin machine
  Fetch pending messages
  Request is pre-authorized and automatically handled
On laptop: Complete connection.
  Device now synchronizes

## Slide 5: QR Code connection: Camera on new Device
Stage 0 (optional)
  QR code with WiFi connection info
Admin device presents QR code with
  PIN code
  Mesh account to connect to
Device reads information, makes connection request
Admin device automatically authorizes
Devices completes connection

## Slide 6: QR Code connection: Camera on Admin device
[Or on device connected to an admin device]
Suited to connection of IoT devices
Manufacturer generates device profile
  Encrypts, places on Web site
  Prints udf: encrypted authenticated resource locator QR code on device
User scans new device using admin device
  Resolves URL, obtains document giving connection info
  The (initial) WiFi SSID the device listens on
  The (initial) Bluetooth connection configuration
  A Mesh Service the device will contact to obtain contact information

## Slide 7: Additional mechanisms
Any connection mechanism can be used provided only that
Device and Mesh are sufficiently mutually authenticated
  112, 132, bit work factor